Wave simulation

Open a terminal window by clicking on the black rectangular icon:

‘Change directory’ to the ‘FramWorkshop’ directory,

cd FramWorkshop

then again into the ‘wave’ directory.

cd wave

Run a simulation of a travelling wave, by running the python program ‘wave.py’, which will show its output as an animation. The simulation represents the string without any friction, air resistance, etc.

python wave.py

Look at the source code using the text editor ‘kate’.

kate wave.py

At the top of the file we import some packages that we will use[1], then define some functions (https://www.w3schools.com/programming/prog_functions.php):
[1] ‘numpy’ (‘Numerical Python’) is the standard Python package for numerical/scientific computing, providing arrays and many maths functions. ‘matplotlib’ is one of the standard Python plotting packages. ‘animatplot’ is a helper package for making animations using matplotlib more easily.
- ‘simulate_wave’ runs our wave simulation and outputs the displacement ‘d’ and velocity ‘v’ along with the simulation grids.
- ‘animate_results’ take ‘d’ and the grids as inputs, and create the animation that you saw already.
- we will come back to ‘animate_results_with_error’ later.

Finally, in the last 10 lines we define some input parameters, and call functions to run and animate the simulation.
Things to do

1. We might expect decreasing the timestep size to make the simulation more accurate. Try changing the setting. What do you see? [Hint: if you decrease the timestep a lot, the animation will take a long time to play. The value of ‘timesteps_per_frame’ sets how many timesteps to jump forward for each frame of the animation (it started at timesteps_per_frame=1 so that every timestep was shown), so increasing this value will speed up the animation.]
  What about increasing the timestep? Is any change you see gradual, or does it appear suddenly for some special value of the timestep?
2. The length of the string is 1 m (defined at the top of the ‘simulate_wave’ function). For the number of grid points in your simulation (‘n_gridpoints’), what is the grid spacing? How does it compare to the timesteps you used in part 1?
   If you change the number of grid points, does it change any special value from part 1?
3. The exact solution for our wave is that the initial profile travels to the right at speed wave_speed without changing shape. This exact solution is output from ‘simulate_wave’ in the ‘exact_d’ variable. Enable the ‘animate_results_with_error’ line by deleting the ‘#’ character that turns the line into a ‘comment’ to see a comparison of our simulation to the exact solution.

   Can you increase the number of grid points in the simulation to get a good match to the exact solution? Be careful, if you increase the number too much, the simulation might take a long time! [Hint: you can stop a running simulation by pressing Ctrl-C.]
  #animate_results(time, grid, d, timesteps_per_frame)
  animate_results_with_error(time, grid, d, exact_d, timesteps_per_frame)
Fusion code: moment_kinetics

The code that John and Sarah work on is called moment_kinetics. It simulates a fusion plasma and is installed on the laptops we are using for this workshop.

Go back to the home directory.

cd

Copy some input files and a plotting script into the moment_kinetics directory.

cp FramWorkshop/moment_kinetics_stuff/* moment_kinetics/

Go into the moment_kinetics directory, and run a simulation using the sound-wave.toml input file that we just copied in.

cd moment_kinetics
./run_moment_kintics.sh sound-wave.toml

The output of this run is stored in some files in the directory runs/sound-wave/. Look at it using the Python plotting script we copied, passing the output file ending with ‘.dfns.h5’.

python plot_moment_kinetics.py runs/sound-wave/sound-wave.dfns.h5

Looking at the ‘pressure’ graph, you should see a standing wave, that gets smaller as time goes on. In this simulation there is mixing between different parts of the plasma that damps the wave, as well as friction between the plasma and some neutral gas that is also present.